## Slide 1: Principles in map making

## Slide 2: How to make sound maps
Thinking Spatially
Basics of Map making
    Map Elements
      Scale,
      Legend,
      Compass,
      Title and Source
Visual considerations when Mapping
    Types of visualisation

## Slide 3
Thinking Spatially
“The most incomprehensible thing about the world is that it is comprehensible”
- Albert Einstein
What’s going on around you?
Source: ICIMOD, 2000

## Slide 4
People who are familiar with HIV/AIDS in Tanzania can visualize the situation. They knows where the problematic areas are, the issues at these localities, and the types of programs in these areas.
We call this a mental map that has been generated from the information stored in the persons mind over the years, consciously or unconsciously.
Source: ICIMOD, 2000
Notes: <number>

## Slide 5
These mental maps are not sufficient if we want to know about the problem in more detail or communicate it to others and make decisions.
The Generals, planners, engineers and so on… all make use of maps and drawings to guide them.
Maps help us –
  to visualize the situation
  to make decisions
  to implement the plans
Maps are powerful tools
Source: ICIMOD, 2000
Notes: <number>

## Slide 6: How does this relate to GIS
GIS is a tool that can allow US to create maps of our data so WE can start
THINKING SPATIALLY
What is GIS
Geographic Information Systems
GIS can
Capture, store, retrieve, analyse and display information based on their LOCATION

## Slide 7
How do Maps Help do this?
– Improve our Understanding of the world!
A map is a picture of a place and gives you better understanding of that place.
Map is a two-dimensional representation of a particular place.
Maps are made for many reasons and therefore they vary in content and context. Different maps show different information.
Different symbols are used to represent the features on earth onto a map, which are explained in the legend. The legend in a map tells what each symbol shows.
So Well Made Maps can Quickly and Easily give
Content and Context
Source: ICIMOD, 2000

## Slide 8
The usefulness of a map depends upon the following factors.
Who is going to use them?
The map audience or the users will influences how a map should look like. A map made for school children will be very different from one made for scientists. Similarly, tourist maps and topographic maps of the same area are very much different in their contents and look as they are made for different users.
What is their purpose?
The purpose of the map determines what features are included and how they are represented. The different purposes such as orientation and navigation, physical planning, management, and education lead to different categories of maps.
Source: ICIMOD 2000

## Slide 9
What is their content?
The usefulness also depends upon the contents of a map. The contents can be seen as primary content (main theme), secondary content (base map information) and supportive content (legends, scale, etc).
What is the scale of the map?
The map scale is the ratio between a distance on a map and the corresponding distance in the terrain. Scale controls the amount of detail and extent of area that can be shown. Scale of the output map is based upon considerations such as - the purpose of the map, needs of the map user, map content, size of the area mapped, accuracy required etc.
Source: ICIMOD 2000

## Slide 10: Summary- Usefulness of the map
How do the following influence the map?
Who is using the Map?
Who is making the Map?
The Purpose
The Content
The Scale

## Slide 11: Important Properties of Maps and GIS
When using GIS or creating Maps there are Four factors that are Important
  Scale
  Legend
  Title
  Source
All affect the Context of Data displayed and How the Data is and can be INTERPRETED

## Slide 12: Scale of a Map
What is scale?
It is the ‘representative fraction’ it states the relationship between the distance on the map and the distance on the ground
Why is Scale so IMPORTANT?
The scale affects the level of detail a map/GIS dataset can show.

## Slide 13
Large-scale maps cover small areas, but can include a higher level of detail than small-scale maps which depict larger areas at lower detail.
There are no precise definitions of large- or small-scale, but for most map users, the following general scale categories apply:
• Large-scale: 1:250 to 1:1,000
• Medium-scale: 1:1,000 to 1:10,000
• Small-scale: 1:10,000 to 1:100,000
• Very Small-scale: 1: 100,000 to above
Map Scale
Source: ICIMOD, 2000

## Slide 14
Small Scale
Large Scale
1:500,000
1:50,000

## Slide 15: Scale
Where is the scale information for GIS datasets
GIS dataset do not state the scale on the map, because you can change the scale (zoom In and Out).
The scale of GIS datasets can be found in the Metadata!!!!
How does scale effect our use of GIS datasets
The scale effects the use of GIS dataset in two ways
  How far we can zoom in and out reliably on a dataset
  Which GIS datasets we can integrate together

## Slide 16: Scale
What are the General rules with Scale issues
  Do not zoom below the scale as stated for the dataset (that is scale at which the data was collected)
  Only integrate GIS dataset that have been collected at the same or at a similar scale
  The maximum scale a dataset should be view is approximately 100 times the Scale that is stated in the Metadata.
  For Example: Data collected at 1:5000 it should not be viewed above 1:500000

## Slide 17: Legend, Title and Source
Legend
Needs to Clearly define the category breakdowns
Title
Needs to define WHAT, WHERE and WHEN is been mapped!
Source
The source for both the Geographic data and Attribute Data

## Slide 18
Title
WHAT,WHERE and WHEN
Legend
Clearly Defined Divisions
Source
Both SPATIAL and ATTRIBUTE sources are stated

## Slide 19: Issues to Remember Maps can LIE!!
Maps are just one person’s representation of the Real World
Like any source of information they can be misleading specially when used out of context
How maps can be deceiving
  Inappropriate Legend
  Inappropriate Scale
Source: ICIMOD, 2000

## Slide 20
Population Density in Tanzania
in 2002 by ward

## Slide 21: Practical
  How to add
  Title – What, Where and When
  Legend – Clear and Precise
  Scale Bar
  Source – Concise
  Compass

## Slide 22: Basic Cartographic Concepts

## Slide 23: Basic Cartographic concepts
Map Design
  Cartographic standards
  Generalization
  Graphic Variables
  Use of Color
  Classification of Data
  Methods of Mapping

## Slide 24
Map making is both science and art.
Maps influence people’s perception of space. This influence is partly because of convention and partly because of the graphics used.
People understand the world differently, express this understanding differently in maps, and gain different understanding from the maps.
Map Design

## Slide 25: Cartographic standards
Basic Map Elements
  Administrative boundaries
    Either Black or Grey
    Higher Administrative unit the thicker the line
  Roads
    Red
    Tracks dashed lines (light red/brown)
  Rivers and Lakes
    Blue
    Streams dashed lines light blue
  What do you think Health Centres should symbolized

## Slide 26
Generalization
Maps contain a certain level of detail depending upon its scale and purpose.
Map Design
Generalization is done normally when the map scale has to be reduced. However, the essence of the contents of original map should be maintained. This implies maintaining geometric and attribute accuracy as well as the presentation quality of the map.
The process of reducing the amount of detail in a map in a meaningful way is called generalization.
Source: ICIMOD 2000

## Slide 27
Size
Value
Texture
Colour
Orientation
Shape
Map Design
Graphic Variables
The differences in the graphic character of symbols give different perceptions to the map reader. These graphic characteristics are termed as graphic variables which can be summarised as size, Lightness or grey value, Grain or texture, Colour, Orientation, and Shape or form.
Source: ICIMOD 2000

## Slide 28
Use of Colour
Colour perception has psychological, physiological and conventional aspects.
It has been noted that it is difficult to perceive colour in small areas, and more contrast is perceived between some colours than between others.
In addition to distinguishing nominal categories, colour differences are also used to show deviations or gradation.
Hue
Saturation
Intensity
Source: ICIMOD 2000

## Slide 29
Classification of Data
The representation of data for mapping will depend on the measurement scale of the data.
Nominal scale: The differences in data are only of qualitative nature, e.g., differences in facility type, land use or geology.
Interval scale: Both the hierarchy and the exact distance is known, but it will not be possible to know the ratios, e.g., the temperature or the altitude values.
Ratio scale: Data can be measured on a ratio measurement scale, e.g., the number of children in a family or income.
Ordinal scale: Only the order of the attribute values is known, such as more than or less than, “small - medium – large” or “cool - tepid - hot”.
Source: ICIMOD 2000

## Slide 30
Mapping Methods
standardized ways of applying graphic variables for rendering information components
based on the measurement scale and nature of the distribution of objects
Chromatic maps:
Renders Categories of areas with different colours. This for nominal scale,
Development Regions of Nepal
Source: ICIMOD 2000

## Slide 31
Access to safe drinking water
Choropleth maps:
Values are calculated for area and expressed as stepped surface, showing a series of values. The order between the classes can be seen.
Isoline maps:
Isoline maps represent continuous phenomena. Isolines connect the points with an equal value and show the trends.
Annual precipitation
Mapping Methods
Source: ICIMOD 2000

## Slide 32
Nominal point data:
Nominal data represented by symbols that are different in shape, orientation or colour.
Absolute proportional method: Discrete absolute values for point locations or areas are represented by proportional symbols.
Major Airports
No. of Biogas Plants
Mapping Methods
Source: ICIMOD 2000

## Slide 33
Diagram maps:
Diagrams are used in the maps to allow comparisons between figures or to visualize temporal trends.
Dot maps:
Dot maps represent point data through symbols. Each dot denote the same quantity. Eg. One Dot = One thousand people.
Population distribution, 1991
Mapping Methods
Source: ICIMOD 2000

## Slide 34
Flowline maps:
Simulate movement using arrow symbols. Arrows indicate route and direction of flows and volume is shown by the relative thickness of the arrow shaft.
Statistical surfaces:
Three dimensional representation of qualitative data such as used in choropleth and isoline maps.
Migration trend
Population growth rate
Mapping Methods
Source: ICIMOD 2000

## Slide 35
New products like electronic atlases, cartographic animations and are coming up in the field of spatial information.
New Map Output Types
With the added potential of digital computers, new ways of visualization and using spatial information are being developed.
These developments allow easy access through the GIS to text documents describing a parcel of land, photographs of the location, or a video clip of the landscape of the study area.
Source: ICIMOD 2000

## Slide 36: Demonstration of Map Making
The process from Question to Map
Determine what type of Map best answers the Question
Set the Classification of the data
Create Output Layout
  Set the Legend, Scale, Title and Source
Output Map

## Slide 37: Summary
Using cartographic standards
Use of graphic symbols
Use of colour
Use of different mapping methods